## Slide 1: Rising Bubble
Kamila Součková
16

## Slide 2: Task
A vertical tube is filled with a viscous fluid. On the bottom of the tube, there is a large air bubble. Study the bubble rising from the bottom to the surface.

## Slide 3: Understanding the Task
A vertical tube is filled with a viscous fluid. On the bottom of the tube, there is a large air bubble. Study the bubble rising from the bottom to the surface.
large = length > width

## Slide 4: Understanding the Task
A vertical tube is filled with a viscous fluid. On the bottom of the tube, there is a large air bubble. Study the bubble rising from the bottom to the surface.
large = length > width
= stable flow

## Slide 5: Understanding the Task
A vertical tube is filled with a viscous fluid. On the bottom of the tube, there is a large air bubble. Study the bubble rising from the bottom to the surface.
large = radius comparable to radius of tube
(length > width)
= stable flow

## Slide 6: Understanding the Task
What to Study:
motion
shape of bubble
Depending on:
volume of bubble V
diameter of tube D
properties of liquid
“Study the bubble”

## Slide 7: Analysis of the SYstem

## Slide 8: Properties of Liquid
 | density | viscosity | surface tension
 | ρ | = resistance to flow dynamic µ kinematic | result of cohesive intermolecular forces minimizes surface area σ
water | 1000 kg/m3 | 1.0 kg/(s·m) (at 20°C) | 71.97 mN/m
oil | 890 kg/m3 | 43.7 kg/(s·m) | 32 mN/m
ethanol | 789 kg/m3 | 0.9 kg/(s·m) | 22.27 mN/m
soap | 1020 kg/m3 | 5 kg/(s·m) | 3 mN/m

## Slide 9: Forces in the System
gravity acting on liquid
gravity acting on bubble
liquid will flow down,
  pushing bubble up
water needs to flow around

## Slide 10: Forces in the System
gravity acting on liquid
gravity acting on bubble
resistance due to viscosity
pressure inside bubble
stresses due to surface tension
and pressure in the liquid
water needs to flow around
liquid will flow down,
  pushing bubble up

## Slide 11: Motion of the bubble

## Slide 12: Speed of rising
stabilized soon due to viscous forces
Chart: time / s
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
v [m/s] | 0.10605 | 0.11247 | 0.12185 | 0.1212 | 0.12525 | 0.12711 | 0.12922 | 0.13067 | 0.12968 | 0.13253 | 0.12912 | 0.12808 | 0.1289 | 0.13172 | 0.13013 | 0.12677 | 0.12929 | 0.12628 | 0.12772 | 0.12405 | 0.12798 | 0.1321 | 0.12746 | 0.12717 | 0.12626
water,
D = 1.4cm

## Slide 13: Speed of rising
Chart: volume of bubble / ml
| 0.15393804002590011 | 0.15393804002590011 | 0.46181412007769984 | 0.53878314009064887 | 6.6193357211136936 | 7.8508400413208905 | 8.4665922014245041 | 9.8520345616576019 | 11.083538881864797 | 12.622919282123787 | 0.76969020012950073 | 2.3090706003884978 | 1.6933184402848984 | 2.0011945203367003 | 2.4630086404143992 | 3.0787608005179994 | 3.6945129606215983 | 4.6181412007769884 | 5.3878314009064878 | 6.6193357211136936 | 14.162299682382784 | 15.701680082641783
v [m/s] | 0.07992 | 0.074906 | 0.074906 | 0.074906 | 0.077369 | 0.077295 | 0.07992 | 0.072661 | 0.074906 | 0.077369 | 0.07992 | 0.077295 | 0.077295 | 0.07992 | 0.077369 | 0.077369 | 0.07992 | 0.074977 | 0.077295 | 0.077369 | 0.07992 | 0.077295
does not depend on bubble volume:
oil,
D = 1.4cm
Chart: volume of bubble / ml
| 0.39584067435231457 | 0.56548667764616278 | 0.84823001646924479 | 3.9584067435231387 | 4.5238934211693023 | 5.0893800988154654 | 5.6548667764616276 | 6.2203534541077898 | 6.785840131753953 | 7.4644241449293478 | 8.2561054936339691 | 9.0477868423386045 | 14.13716694115406 | 1.1309733552923256 | 1.4702653618800241 | 1.809557368467722 | 2.2619467105846511 | 2.9405307237600482 | 3.3929200658769787
 | 0.066023 | 0.061846 | 0.064935 | 0.061846 | 0.062832 | 0.063882 | 0.062832 | 0.063882 | 0.06089 | 0.063882 | 0.062832 | 0.063882 | 0.062832 | 0.06089 | 0.067149 | 0.064935 | 0.061846 | 0.063882 | 0.062832
water,
D = 0.9cm

## Slide 14: Speed of Rising: Different Liquids, Tubes
Chart: velocity / m·s-1
| water | oil | ethanol | soap
D = 0.94cm | 0.063926 | 0.057292 | 0.094178 | 0
D = 1.40cm | 0.10638 | 0.096154 | 0.11905 | 0.025641
D = 1.56cm | 0.1275 | 0.11724 | 0.14571 | 0.039231
 | density ρ | dynamic viscosity µ | surface tension σ
water | 1000 kg/m3 | 1.0 kg/(s·m) | 71.97 mN/m
oil | 890 kg/m3 | 43.7 kg/(s·m) | 32 mN/m
ethanol | 789 kg/m3 | 0.9 kg/(s·m) | 22.27 mN/m
soap | 1020 kg/m3 | 5 kg/(s·m) | 3 mN/m
Notes: vidime ze pre rozne kvapaliny s roznymi vlastnostami su rozne rychlosti, je to cele zlozite… podme to popisat!

## Slide 15: Description of Bubble Rising
v
u(z)
w
z

## Slide 16: Starting with…
unknowns:
  velocity profile of the thin layer flowing around the bubble u(z)
  velocity of bubble v
  width of layer flowing around bubble w
v
u(z)
w

## Slide 17: Starting with…
unknowns:
  velocity profile of the thin layer flowing around the bubble u(z)
  velocity of bubble v
  width of layer flowing around bubble w
  gravity + shear force →
v
u(z)
w
w
Notes: ok, mam u(z)… (medzera) teraz podme rozmyslat nad tym, ako dostat hentie 2 ciselka
nemam popisane veliciny

## Slide 18: Starting with…
unknowns:
  velocity profile of the thin layer flowing around the bubble u(z)
  gravity + shear force →
  velocity of bubble v
  width of layer flowing around bubble w
  continuity (liquid ↓ = air ↑ ) →
v
u(z)
w

## Slide 19: Starting with…
unknowns:
  velocity profile of the thin layer flowing around the bubble u(z)
  gravity + shear force →
  velocity of bubble v
  width of layer flowing around bubble w
  continuity (liquid ↓ = air ↑ ) →
v
u(z)
h
Notes: 3rd equation

## Slide 20: Combine the equations
velocity profile
continuity
tried to find 3rd equation → no analytical solution; very difficult to solve numerically

## Slide 21: Bubble Rising: Experimentally Prove Expected v/h3
need to find h → measure change in bubble length
expectation:
“head”
L
cylindrical “body”

## Slide 22: Bubble Rising: Experimentally Prove Expected v/h3
Chart: length of bubble at rest L0 / cm
| 4.9000000000000004 | 5.7 | 6.1 | 6.6 | 7.2 | 7.3 | 9 | 9.9 | 10.7 | 11.5 | 12 | 12.7 | 13.8 | 15.3 | 15.6 | 16.7 | 17.2 | 18 | 18.399999999999999 | 18.5 | 20 | 20.100000000000001 | 21.15000000000002 | 22 | 22.9 | 23.1 | 24.1 | 24.5 | 25.5 | 27.5 | 28.4 | 30.2 | 30.6 | 30.85 | 32.5 | 34.5
L_r [cm] | 6.0606 | 7.0707 | 8.0808 | 8.0808 | 9.0909 | 9.0909 | 11.1111 | 12.6263 | 13.6364 | 14.6465 | 15.1515 | 15.6566 | 16.6667 | 17.6768 | 18.6869 | 19.697 | 20.7071 | 23.2323 | 23.2323 | 22.7273 | 24.7475 | 24.2424 | 25.7576 | 26.2626 | 28.2828 | 28.2828 | 29.2929 | 29.798 | 31.3131 | 32.8283 | 33.3333 | 35.8586 | 35.8586 | 35.8586 | 37.3737 | 39.3939
expectation:
L = 1.15L0 + 1.06

## Slide 23: Bubble Rising: Experimentally Prove Expected v/h3
Prolonging of the cylindrical part:

## Slide 24: Bubble Rising: Experimentally Prove Expected v/h3
Pluding experimental velocity:

## Slide 25: Bubble Rising: Experimentally Prove Expected v/h3
Theory correlates with experiment
✓

## Slide 26: Speed of Rising: More Experiments

## Slide 27: Isolate Parameter: Viscosity
Chart: dynamic viscosity / kg/(s·m)
| 0.62582855224272005 | 0.66014738634237013 | 0.53269418131711976 | 0.58519597216592012 | 0.61516374163757037 | 0.64253120195137314 | 0.53269418131711976 | 0.55786247527757005 | 0.5948675504812504 | 0.63686593610477016 | 0.6724378811835201 | 0.71220337098125008 | 0.45305371766877012 | 0.5018119355187205 | 0.97550199839517004 | 0.62582855224272005 | 0.69844032275712009 | 0.74138671731597006 | 0.80717960837117009 | 0.86398038241232 | 1.1427804494812501 | 1.0006554512000001 | 1.1747621625531202 | 1.1427804494812501 | 1.0268464002439699 | 0.8845068007812501
v [m/s] | 0.080208 | 0.071305 | 0.096249 | 0.083353 | 0.071588 | 0.069458 | 0.062771 | 0.07114 | 0.068343 | 0.068335 | 0.067839 | 0.074946 | 0.065611 | 0.083353 | 0.057881 | 0.069458 | 0.049091 | 0.07114 | 0.054663 | 0.05731 | 0.041847 | 0.047586 | 0.035022 | 0.051888 | 0.041082 | 0.037483
hot water: viscosity changes with temperature much more than density, surface tension
Chart: temperature / °C
| 0 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Table values | 1.787 | 1.519 | 1.307 | 1.002 | 0.798 | 0.653 | 0.547 | 0.467 | 0.404 | 0.355 | 0.315 | 0.282
27
http://www.engineeringtoolbox.com/water-dynamic-kinematic-viscosity-d_596.html

## Slide 28: Shape of Bubbles

## Slide 29: Characterizing the System
Reynolds number: viscous vs inertial forces
Eötvös (Bond) number: surface tension vs gravitational forces
Notes: velky eotvos znamena male sigmy → bude to negulate

## Slide 30: Shapes of Bubble
Re | Eo | 5 | 10 | 20
5 |  |  |  | 
10 |  |  |  | 
20 |  |  |  | 
honey
shampoo
water
oil
?
petrol

## Slide 31: Shapes of Bubble: Comparison with Literature (no tubes)
source: Jinsong Hua, Jing Lou, 2007, Numerical simulation of bubble rising in viscous liquid

## Slide 32: Mystery: Tail
shampoo has a clearly visible tail
sometimes a small tail can be observed in honey too (esp. when not exactly vertical)
not mentioned in literature
our explanation: very viscous → does not “fill” the bottom fast enough

## Slide 33: Conclusion

## Slide 34: Conclusion
gravity acting on liquid
gravity acting on bubble
pressure inside bubble
stresses due to surface tension
liquid will flow down,
pushing bubble up
resistance due to viscosity
force analysis

## Slide 35: Conclusion
w
force analysis (gravity, viscosity, pressure, surface tension)
flow in the tube

## Slide 36: Conclusion
force analysis (gravity, viscosity, pressure, surface tension)
flow in the tube (velocity profile)
speed of rising
theory correlates with experiment
✓

## Slide 37: Conclusion
force analysis (gravity, viscosity, pressure, surface tension)
flow in the tube (velocity profile)
speed of rising (theory + correlating exp for various parameters)
shapes of bubbles

## Slide 38: Conclusion
force analysis (gravity, viscosity, pressure, surface tension)
flow in the tube (velocity profile)
speed of rising (theory+correlating exp for various parameters)
shapes of bubbles (depending on Re, Eo)
“study the bubble”
✓

## Slide 39: Thank you for your attention!
force analysis (gravity, viscosity, pressure, surface tension)
flow in the tube (velocity profile)
speed of rising (theory+correlating exp for various parameters)
shapes of bubbles (depending on Re, Eo)
“study the bubble”
✓

## Slide 40
16. Rising Bubble
Kamila Součková

## Slide 41: Appendix

## Slide 42: Characteristics of the System: Flow
Reynolds number: defines relative importance of viscous and inertial forces
  in our case always ⇒ flow is laminar

## Slide 43: Reynolds number
Refound in articles =
Reussualy expected =
Estimations from continuity equation:
=
v – velocity of bubble
u – velocity of liquid
R- radius of bubble
ρ- density of liquid
µ - viscosity of liquid
w- thickness of layer
R
w
v
u
= Refound in articles

## Slide 44: Velocity Profile
velocity profile of the thin layer flowing around the bubble u(z)
gravity + shear force
⇒
(holds for laminar flow and sufficiently long bubbles)
w
source: Zbierka FX (collection of solved physics problems)

## Slide 45: Velocity of Rising, Width of Layer
velocity of bubble v
width of layer flowing around bubble h
continuity
amount of liquid going down = amount of air going up
integrating + simplifying *
velocity profile
=
* simplification: thin layer
(approximation:
cylinder)

## Slide 46: Description of Bubble Rising
velocity profile
continuity
(const for a given liquid & tube)

## Slide 47: Beyond the Ratio
→ experiment: v depending on R
?
?
Chart: radius /cm
| 0.81 | 0.54500000000000004 | 0.75 | 1.18
∅ of 3 values | 0.20161 | 0.084459 | 0.14045 | 0.39683

## Slide 48: Beyond the Ratio
→ experiment: v depending on R
?
?
Chart: radius /cm
| 0.81 | 0.54500000000000004 | 0.75000000000000078 | 1.1800000000000013
∅ of 3 values | 0.20161 | 0.084459 | 0.14045 | 0.39683
2
1