## Slide 1: Carbon Microphone
Marco Bodnár
9.

## Slide 2: Task
For many years, a design of microphone has involved the use of carbon granules. Varying pressure on the granules produced by incident sound waves produces an electrical output signal. Investigate the components of such a device and determine its characteristics.

## Slide 3: Basic scheme
Notes: Spomenut ze chamber je non conducting

## Slide 4: Basic scheme and principle
Resistance decreases
Current is dynamic Voltage drop across resistor is dynamic

## Slide 5: Factory assembled microphone

## Slide 6
Microphone base
Elastic membrane
Cover
Chamber
Carbon powder
Covering membrane
Notes: Elastic membrane is glued to chamber

## Slide 7: Voltage is needed
MICROPHONE IS PASSIVE
- WITHOUT VOLTAGE APPLIED – NO VOLTAGE CHANGE CAN BE MEASURED
Dynamic resistance
Dynamic voltage, current
Measureable
Notes: Some computers have voltage in jack connector about 2 V – sufficient for factory made mic, but not for out.. Bez voltage by pocitac nemal co merat

## Slide 8: Membrane
Radius – change in frequency characteristics
Weight – as light as possible
Elasticity
Notes: Thick enough – do not break, but not too thick – har to make oscilateSubwooofer – our prediction since we do not have ability to change membrane – thick heavy – difficult to make it oscilate..

## Slide 9: Why carbon powder?
Bad conductor
(in comparison with metals)
  - sensitivity of microphone - ideally no added substances
Stable - does not change structure with temperature or other conditions*
*to a certain extent
Very high sensitivity (of its resistivity) to pressure change
Notes: Necessary bad conductor.. If not eg gold changes would be unobservable – but the most important is its sensitivity- easily discernible changes – sum je ovplyvneny aj tvarom uhliku
So stable – even used by astronauts – it has to be clean – important otherwise noise is present – not additional substances- niekedy som videl ako dry lubricant silicum powder

## Slide 10: Covers
Protect inner parts of microphone (not necessary for correct functioning)
Front foil – protects from dirt
Back cover – protects from mechanical damage

## Slide 11: Hole in diaphragm
Hole in diaphragm used for pressure equalisation
Without hole – overpressure inside the microphone – diaphragm bulks out
With hole – equal pressure inside the microphone and outside– diaphragm remains same
Notes: Membrane is glued – isolated – it needs hole – spomenut ze budeme skumat efekt

## Slide 12
Now that we know how it works…
…we will try to make our own.

## Slide 13
Flexible membrane
Conducting pistons
Voltage source
Switch
Resistor
Chamber
Notes: Voltage source is needed, because the resistance is very high and 2 V is insufficient -external voltage source and resistance

## Slide 14
Membrane
Chamber
Resistor
Voltage source

## Slide 15: Home made record
Home made
R=5000Ω
Further measurements with factory assembled microphone only.
Home made
Notes: Vybrali sme naschval pesnicku s lower frequency – vyssie nepocujeme ni tu.. Ticho – ukazat na graph
Komentovat higher frequencies nie pocutelne … a nepouzivli sme ho lebo bol nepouzitelny prakticky bolo do neho velmi hucat z blizky – na meranie nevhodny..
Used our because non stable this was the best we could after many times –granules might be better – from some other electronic device equipment (filter – activated)- not made for this purpose

## Slide 16: Apparatus
Sound analysis
Sound production
Loudness meter

## Slide 17: Frequency response at 94 dB
Resonant frequencies of mechanical parts
Does the hole has an effect on the frequency response?
Chart: Frequency [Hz]
| 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800 | 10000
Original hole | -80 | -73.9794 | -64.437 | -54.8945 | -42.8534 | -32.9563 | -36.1934 | -41.1103 | -42.6154 | -47.535 | -50.3958 | -49.1186 | -37.523 | -34.6566 | -30.995 | -31.734 | -27.4118 | -33.3109 | -24.1802 | -20.7621 | -21.5559 | -27.2103 | -26.8207 | -23.3882 | -28.7541 | -29.4991 | -37.8558 | -34.9429 | -24.0824 | -25.1298 | -23.3243 | -25.3521 | -25.4981 | -28.8019 | -30.9031 | -34.9916 | -36.1375 | -34.751 | -40 | -41.6184 | -46.0206 | -42.6154 | -39.9136 | -46.9357 | -45.1927 | -44.1522 | -44.8825 | -50.4576 | -50.752 | -50.1186 | -50.984 | -52.446 | -54.875 | -57.143 | -61.9382 | -66.0206 | -70.4576 | -80
Notes: Cavities in graph - how does the pattern changes when hole is changed?

## Slide 18: Frequency response at 94 dB - hole effect
Chart: Frequency [Hz]
| 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800
Without hole | -73.9794 | -63.098 | -61.9382 | -57.0774 | -41.6184 | -34.5632 | -37.8558 | -42.7335 | -41.2096 | -44.2934 | -51.8945 | -52.391 | -38.6363 | -37.7882 | -35.6503 | -38.5624 | -36.7726 | -39.5762 | -30.7221 | -26.5212 | -27.4938 | -27.639 | -28.0681 | -24.5683 | -30.995 | -33.8501 | -40.2646 | -35.8635 | -26.8398 | -29.8429 | -26.9744 | -30.8424 | -31.1818 | -31.4373 | -32.7654 | -33.7227 | -34.0229 | -31.3086 | -33.8074 | -36.5363 | -41.4116 | -42.4988 | -41.5144 | -42.264 | -43.486 | -44.004 | -44.2934 | -48.8739 | -50.4576 | -53.5556 | -54.4249 | -55.9176 | -60 | -66.0206 | -70.4576 | -73.9794 | -80
Notes: Cavity in the graph we glued the original hole

## Slide 19: Frequency response at 94 dB - hole effect
Chart: Frequency [Hz]
| 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800
Radius 1 mm | -80 | -73.9794 | -60 | -36.082 | -31.3727 | -38.6363 | -37.1397 | -42.8534 | -43.4785 | -47.9588 | -45.3521 | -33.2708 | -29.0199 | -25.1612 | -32.1461 | -31.4373 | -33.4733 | -27.2702 | -27.3711 | -27.4938 | -31.405 | -29.1435 | -23.3754 | -25.4005 | -26.4114 | -34.1107 | -36.5363 | -31.5679 | -27.8509 | -28.0461 | -30.8727 | -29.6825 | -34.0667 | -32.995 | -35.1392 | -39.7433 | -42.2702 | -45.6799 | -46.1961 | -46.0206 | -42.7335 | -42.3837 | -47.7443 | -47.1309 | -47.3306 | -50.4576 | -52.7654 | -54.8945 | -57.0774 | -56.4782 | -60 | -64.437 | -67.9588 | -70.4576 | -70.4576 | -80

## Slide 20: Frequency response at 94 dB - hole effect
Chart: Frequency [Hz]
| 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800 | 10000
Radius 2 mm | -80 | -58.4164 | -32.111 | -37.9926 | -39.0935 | -34.9429 | -41.5374 | -46.583 | -47.2934 | -36.9542 | -34.3793 | -28.0461 | -32.2879 | -38.2019 | -32.8795 | -28.4502 | -31.5024 | -29.4217 | -25.3521 | -23.4526 | -21.3404 | -21.9491 | -27.3105 | -33.2708 | -31.245 | -26.9551 | -30.9031 | -28.0681 | -31.1191 | -29.5511 | -29.897 | -31.3727 | -34.1549 | -31.5679 | -31.8013 | -33.5144 | -35.9721 | -37.0774 | -38.7108 | -41.0122 | -44.437 | -41.6184 | -43.3498 | -46.1961 | -44.437 | -48.1787 | -54.4249 | -57.7211 | -58.4164 | -60 | -59.1721 | -67.9588 | -70.4576 | -73.9794 | -80

## Slide 21
Chart: Frequency [Hz]
| 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800
Without hole | -73.9794 | -63.098 | -61.9382 | -57.0774 | -41.6184 | -34.5632 | -37.8558 | -42.7335 | -41.2096 | -44.2934 | -51.8945 | -52.391 | -38.6363 | -37.7882 | -35.6503 | -38.5624 | -36.7726 | -39.5762 | -30.7221 | -26.5212 | -27.4938 | -27.639 | -28.0681 | -24.5683 | -30.995 | -33.8501 | -40.2646 | -35.8635 | -26.8398 | -29.8429 | -26.9744 | -30.8424 | -31.1818 | -31.4373 | -32.7654 | -33.7227 | -34.0229 | -31.3086 | -33.8074 | -36.5363 | -41.4116 | -42.4988 | -41.5144 | -42.264 | -43.486 | -44.004 | -44.2934 | -48.8739 | -50.4576 | -53.5556 | -54.4249 | -55.9176 | -60 | -66.0206 | -70.4576 | -73.9794 | -80
Original hole | -80 | -73.9794 | -64.437 | -54.8945 | -42.8534 | -32.9563 | -36.1934 | -41.1103 | -42.6154 | -47.535 | -50.3958 | -49.1186 | -37.523 | -34.6566 | -30.995 | -31.734 | -27.4118 | -33.3109 | -24.1802 | -20.7621 | -21.5559 | -27.2103 | -26.8207 | -23.3882 | -28.7541 | -29.4991 | -37.8558 | -34.9429 | -24.0824 | -25.1298 | -23.3243 | -25.3521 | -25.4981 | -28.8019 | -30.9031 | -34.9916 | -36.1375 | -34.751 | -40 | -41.6184 | -46.0206 | -42.6154 | -39.9136 | -46.9357 | -45.1927 | -44.1522 | -44.8825 | -50.4576 | -50.752 | -50.1186 | -50.984 | -52.446 | -54.875 | -57.143 | -61.9382 | -66.0206 | -70.4576 | -80
Radius 1 mm | -80 | -73.9794 | -60 | -36.082 | -31.3727 | -38.6363 | -37.1397 | -42.8534 | -43.4785 | -47.9588 | -45.3521 | -33.2708 | -29.0199 | -25.1612 | -32.1461 | -31.4373 | -33.4733 | -27.2702 | -27.3711 | -27.4938 | -31.405 | -29.1435 | -23.3754 | -25.4005 | -26.4114 | -34.1107 | -36.5363 | -31.5679 | -27.8509 | -28.0461 | -30.8727 | -29.6825 | -34.0667 | -32.995 | -35.1392 | -39.7433 | -42.2702 | -45.6799 | -46.1961 | -46.0206 | -42.7335 | -42.3837 | -47.7443 | -47.1309 | -47.3306 | -50.4576 | -52.7654 | -54.8945 | -57.0774 | -56.4782 | -60 | -64.437 | -67.9588 | -70.4576 | -70.4576 | -80
Radius 2 mm | -80 | -58.4164 | -32.111 | -37.9926 | -39.0935 | -34.9429 | -41.5374 | -46.583 | -47.2934 | -36.9542 | -34.3793 | -28.0461 | -32.2879 | -38.2019 | -32.8795 | -28.4502 | -31.5024 | -29.4217 | -25.3521 | -23.4526 | -21.3404 | -21.9491 | -27.3105 | -33.2708 | -31.245 | -26.9551 | -30.9031 | -28.0681 | -31.1191 | -29.5511 | -29.897 | -31.3727 | -34.1549 | -31.5679 | -31.8013 | -33.5144 | -35.9721 | -37.0774 | -38.7108 | -41.0122 | -44.437 | -41.6184 | -43.3498 | -46.1961 | -44.437 | -48.1787 | -54.4249 | -57.7211 | -58.4164 | -60 | -59.1721 | -67.9588 | -70.4576 | -73.9794 | -80
Frequency response at 94 dB - hole effect
There is no hole effect
Notes: Resonant freq dole lebo trasenie zhorsi nahravaciu schopnost - su tam nejake vykyvy, kde original nie je najlepsi (mal by byt lebo neposkodeni) prave kvoli poskodeniu je to roztrasene

## Slide 22
Chart: Frequency [Hz]
| 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800
Without hole | -73.9794 | -63.098 | -61.9382 | -57.0774 | -41.6184 | -34.5632 | -37.8558 | -42.7335 | -41.2096 | -44.2934 | -51.8945 | -52.391 | -38.6363 | -37.7882 | -35.6503 | -38.5624 | -36.7726 | -39.5762 | -30.7221 | -26.5212 | -27.4938 | -27.639 | -28.0681 | -24.5683 | -30.995 | -33.8501 | -40.2646 | -35.8635 | -26.8398 | -29.8429 | -26.9744 | -30.8424 | -31.1818 | -31.4373 | -32.7654 | -33.7227 | -34.0229 | -31.3086 | -33.8074 | -36.5363 | -41.4116 | -42.4988 | -41.5144 | -42.264 | -43.486 | -44.004 | -44.2934 | -48.8739 | -50.4576 | -53.5556 | -54.4249 | -55.9176 | -60 | -66.0206 | -70.4576 | -73.9794 | -80
Original hole | -80 | -73.9794 | -64.437 | -54.8945 | -42.8534 | -32.9563 | -36.1934 | -41.1103 | -42.6154 | -47.535 | -50.3958 | -49.1186 | -37.523 | -34.6566 | -30.995 | -31.734 | -27.4118 | -33.3109 | -24.1802 | -20.7621 | -21.5559 | -27.2103 | -26.8207 | -23.3882 | -28.7541 | -29.4991 | -37.8558 | -34.9429 | -24.0824 | -25.1298 | -23.3243 | -25.3521 | -25.4981 | -28.8019 | -30.9031 | -34.9916 | -36.1375 | -34.751 | -40 | -41.6184 | -46.0206 | -42.6154 | -39.9136 | -46.9357 | -45.1927 | -44.1522 | -44.8825 | -50.4576 | -50.752 | -50.1186 | -50.984 | -52.446 | -54.875 | -57.143 | -61.9382 | -66.0206 | -70.4576 | -80
Radius 1 mm | -80 | -73.9794 | -60 | -36.082 | -31.3727 | -38.6363 | -37.1397 | -42.8534 | -43.4785 | -47.9588 | -45.3521 | -33.2708 | -29.0199 | -25.1612 | -32.1461 | -31.4373 | -33.4733 | -27.2702 | -27.3711 | -27.4938 | -31.405 | -29.1435 | -23.3754 | -25.4005 | -26.4114 | -34.1107 | -36.5363 | -31.5679 | -27.8509 | -28.0461 | -30.8727 | -29.6825 | -34.0667 | -32.995 | -35.1392 | -39.7433 | -42.2702 | -45.6799 | -46.1961 | -46.0206 | -42.7335 | -42.3837 | -47.7443 | -47.1309 | -47.3306 | -50.4576 | -52.7654 | -54.8945 | -57.0774 | -56.4782 | -60 | -64.437 | -67.9588 | -70.4576 | -70.4576 | -80
Radius 2 mm | -80 | -58.4164 | -32.111 | -37.9926 | -39.0935 | -34.9429 | -41.5374 | -46.583 | -47.2934 | -36.9542 | -34.3793 | -28.0461 | -32.2879 | -38.2019 | -32.8795 | -28.4502 | -31.5024 | -29.4217 | -25.3521 | -23.4526 | -21.3404 | -21.9491 | -27.3105 | -33.2708 | -31.245 | -26.9551 | -30.9031 | -28.0681 | -31.1191 | -29.5511 | -29.897 | -31.3727 | -34.1549 | -31.5679 | -31.8013 | -33.5144 | -35.9721 | -37.0774 | -38.7108 | -41.0122 | -44.437 | -41.6184 | -43.3498 | -46.1961 | -44.437 | -48.1787 | -54.4249 | -57.7211 | -58.4164 | -60 | -59.1721 | -67.9588 | -70.4576 | -73.9794 | -80
Frequency response at 94 dB - hole effect
Low frequencies (speech)
- Low sensitivity
- Low quality of recording?
Notes: Resonant freq dole lebo trasenie zhorsi nahravaciu schopnost - su tam nejake vykyvy, kde original nie je najlepsi (mal by byt lebo neposkodeni) prave kvoli poskodeniu je to roztrasene

## Slide 23: Hi, how are you…? Speech record
Factory made microphone
Actually, not that bad !
Notes: Rec je na uzkom range frequencies – podobnu citlivost – pesnicka nie je na uzkom 100 – 1000, slaba citlivost
V nahravke reci vidime ze kvalita zvuku z microphone je lepsia

## Slide 24
Chart: Frequency [Hz]
| 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1200 | 1300 | 1400 | 1500 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000 | 5200 | 5400 | 5600 | 5800 | 6000 | 6200 | 6400 | 6600 | 6800 | 7000 | 7200 | 7400 | 7600 | 7800 | 8000 | 8200 | 8400 | 8600 | 8800 | 9000 | 9200 | 9400 | 9600 | 9800
Without hole | -73.9794 | -63.098 | -61.9382 | -57.0774 | -41.6184 | -34.5632 | -37.8558 | -42.7335 | -41.2096 | -44.2934 | -51.8945 | -52.391 | -38.6363 | -37.7882 | -35.6503 | -38.5624 | -36.7726 | -39.5762 | -30.7221 | -26.5212 | -27.4938 | -27.639 | -28.0681 | -24.5683 | -30.995 | -33.8501 | -40.2646 | -35.8635 | -26.8398 | -29.8429 | -26.9744 | -30.8424 | -31.1818 | -31.4373 | -32.7654 | -33.7227 | -34.0229 | -31.3086 | -33.8074 | -36.5363 | -41.4116 | -42.4988 | -41.5144 | -42.264 | -43.486 | -44.004 | -44.2934 | -48.8739 | -50.4576 | -53.5556 | -54.4249 | -55.9176 | -60 | -66.0206 | -70.4576 | -73.9794 | -80
Original hole | -80 | -73.9794 | -64.437 | -54.8945 | -42.8534 | -32.9563 | -36.1934 | -41.1103 | -42.6154 | -47.535 | -50.3958 | -49.1186 | -37.523 | -34.6566 | -30.995 | -31.734 | -27.4118 | -33.3109 | -24.1802 | -20.7621 | -21.5559 | -27.2103 | -26.8207 | -23.3882 | -28.7541 | -29.4991 | -37.8558 | -34.9429 | -24.0824 | -25.1298 | -23.3243 | -25.3521 | -25.4981 | -28.8019 | -30.9031 | -34.9916 | -36.1375 | -34.751 | -40 | -41.6184 | -46.0206 | -42.6154 | -39.9136 | -46.9357 | -45.1927 | -44.1522 | -44.8825 | -50.4576 | -50.752 | -50.1186 | -50.984 | -52.446 | -54.875 | -57.143 | -61.9382 | -66.0206 | -70.4576 | -80
Radius 1 mm | -80 | -73.9794 | -60 | -36.082 | -31.3727 | -38.6363 | -37.1397 | -42.8534 | -43.4785 | -47.9588 | -45.3521 | -33.2708 | -29.0199 | -25.1612 | -32.1461 | -31.4373 | -33.4733 | -27.2702 | -27.3711 | -27.4938 | -31.405 | -29.1435 | -23.3754 | -25.4005 | -26.4114 | -34.1107 | -36.5363 | -31.5679 | -27.8509 | -28.0461 | -30.8727 | -29.6825 | -34.0667 | -32.995 | -35.1392 | -39.7433 | -42.2702 | -45.6799 | -46.1961 | -46.0206 | -42.7335 | -42.3837 | -47.7443 | -47.1309 | -47.3306 | -50.4576 | -52.7654 | -54.8945 | -57.0774 | -56.4782 | -60 | -64.437 | -67.9588 | -70.4576 | -70.4576 | -80
Radius 2 mm | -80 | -58.4164 | -32.111 | -37.9926 | -39.0935 | -34.9429 | -41.5374 | -46.583 | -47.2934 | -36.9542 | -34.3793 | -28.0461 | -32.2879 | -38.2019 | -32.8795 | -28.4502 | -31.5024 | -29.4217 | -25.3521 | -23.4526 | -21.3404 | -21.9491 | -27.3105 | -33.2708 | -31.245 | -26.9551 | -30.9031 | -28.0681 | -31.1191 | -29.5511 | -29.897 | -31.3727 | -34.1549 | -31.5679 | -31.8013 | -33.5144 | -35.9721 | -37.0774 | -38.7108 | -41.0122 | -44.437 | -41.6184 | -43.3498 | -46.1961 | -44.437 | -48.1787 | -54.4249 | -57.7211 | -58.4164 | -60 | -59.1721 | -67.9588 | -70.4576 | -73.9794 | -80
Frequency response at 94 dB - hole effect
Let’s record these frequencies - song
Notes: Opat ked sa na to pozrieme…

## Slide 25: Song record
Factory assembled
R=100Ω
Song has significantly worse quality
How is it possible?
Factory made
Wide range of frequencies
possibly irregular input from microphone – different amplitude response
Let’s investigate amplitude dependence of microphone
Notes: Used our because non stable this was the best we could after many times –granules might be better – from some other electronic device equipment (filter – activated)- not made for this purpose
Home made similar to factrory, due to low - zvukovka z toho robi chaos---

## Slide 26
Static amplitude dependence
Turning screw increases pressure
Conductivity vs. pressure measurement

## Slide 27
Static amplitude dependence
Chart: Turns
| 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0.0058824 | 0.0074074 | 0.0083333 | 0.011111 | 0.015385 | 0.022222 | 0.028571
Response is non-linear
Let’s look at the amplitude characteristics
Notes: Zastavit a povedat co to je? Co to znamena… We expect the microphone to record sound and its loudness reliably, it means that if I increase input loudness by 10 dB the recorded loudness also increases by 10 dB

## Slide 28: Amplitude response characteristics
Chart: 
| 85 | 87 | 89 | 91 | 93 | 95 | 97 | 99 | 101 | 103
 | -90 | -88 | -86 | -84 | -82 | -80 | -78 | -76 | -74 | -72
 | -69.9 | -70.4 | -70.9 | -73.7 | -74.6 | -75.2 | -77.2 | -81.9 | -94.1 | -95.1 | -95.2 | -86.4 | -79.2 | -78.8 | -79.9 | -81 | -78 | -73.9 | -89.4 | -85.4 | -82
Chart: 
| 98.3 | 98.8 | 99.3 | 97.7 | 97.7 | 97.7 | 97.3 | 94.3 | 90 | 86.5 | 88.9 | 92.3 | 97.3 | 98.6 | 96.6 | 94.7 | 94.7 | 96.5 | 89.3 | 92 | 93.7
 | -69.9 | -70.4 | -70.9 | -73.7 | -74.6 | -75.2 | -77.2 | -81.9 | -94.1 | -95.1 | -95.2 | -86.4 | -79.2 | -78.8 | -79.9 | -81 | -78 | -73.9 | -89.4 | -85.4 | -82
Slope 1
The slope is different than 1 for log-log graph
– non-linear characteristics
100Hz
Notes: Cim hlasnejsie poviem tym hlas nahram ale coef mimo 1 ..

## Slide 29: Amplitude response characteristics
Chart: Loudness [dB]
| 73.8 | 75.3 | 76.8 | 78.3 | 79.8 | 81.3 | 82.8 | 84.3 | 85.8 | 87.3 | 88.8 | 90.3 | 91.8 | 93.3 | 94.8 | 96.3 | 97.8 | 99.3
 | -94 | -92.5 | -91 | -89.5 | -88 | -86.5 | -85 | -83.5 | -82 | -80.5 | -79 | -77.5 | -76 | -74.5 | -73 | -71.5 | -70 | -68.5
 | -59.2 | -60.5 | -71.6 | -65.8 | -68.2 | -67.1 | -73.7 | -84.6 | -68.4 | -75.8 | -98.5 | -82.4 | -84.2 | -76.1 | -86.3 | -87.4 | -87.1 | -93.72 | -93.2
220Hz

## Slide 30: Amplitude response characteristics
Chart: Loudness [dB]
| 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
 | -109 | -104 | -99 | -94 | -89 | -84 | -79 | -74 | -69 | -64 | -59 | -54 | -49
 | -42.4 | -38 | -40.2 | -37.3 | -28.4 | -28.1 | -29.1 | -33.2 | -45.5 | -81.2 | -74.8 | -45.7 | -58.9 | -52.5 | -69.3 | -72.6 | -65.6 | -68.9 | -69.9 | -85.8 | -94 | -27.3 | -27.6 | -27.2 | -46.1 | -46.6 | -37.1 | -33.2
y = 1,375x - 165,16
440Hz
Slope 1

## Slide 31: Amplitude response characteristics
Chart: Loudness [dB]
| 60.8 | 66 | 71.2 | 76.400000000000006 | 81.599999999999994 | 86.8 | 92 | 97.2 | 102.4
 | -98 | -92.8 | -87.6 | -82.4 | -77.2 | -72 | -66.8 | -61.6 | -56.4
 | -53 | -46 | -41.1 | -49.7 | -54.8 | -57 | -58.2 | -51 | -49.3 | -48.7 | -34.1 | -34.9 | -48.7 | -44.4 | -35.8 | -48.4 | -33.8 | -35.7 | -37.4 | -40.2 | -71.6 | -81 | -98 | -74.9 | -85.3 | -89.9 | -78
1000Hz
y = 1,7228x - 208,05
Slope 1

## Slide 32: Amplitude response characteristics
Chart: Loudness [dB]
| 38 | 40 | 42 | 44 | 46 | 48 | 50 | 52 | 54 | 56 | 58 | 60 | 62 | 64 | 66 | 68 | 70 | 72 | 74 | 76 | 78 | 80 | 82 | 84 | 86 | 88 | 90 | 92 | 94 | 96 | 98 | 100
 | -58.6 | -56.6 | -54.6 | -52.6 | -50.6 | -48.6 | -46.6 | -44.6 | -42.6 | -40.6 | -38.6 | -36.6 | -34.6 | -32.6 | -30.6 | -28.6 | -26.6 | -24.6 | -22.6 | -20.6 | -18.6 | -16.6 | -14.6 | -12.6 | -10.6 | -8.6 | -6.6 | -4.6 | -2.6 | -0.6 | 1.4 | 3.4
 | -20.3 | -18.2 | -18.6 | -18.3 | -21 | -19.2 | -31 | -23.5 | -23 | -21.6 | -22.8 | -24.4 | -19.1 | -18.8 | -29.3 | -34.2 | -33.5 | -58.6 | -39.2 | -52 | -54 | -34.5 | -55 | -45.5 | -37.1 | -44.3
3200Hz
y = 0,6554x - 83,392
Slope 1

## Slide 33: Comparison for different frequencies
Chart: Loudness [dB]
| 98.3 | 98.8 | 99.3 | 97.7 | 97.7 | 97.7 | 97.3 | 94.3 | 90 | 86.5 | 88.9 | 92.3 | 97.3 | 98.6 | 96.6 | 94.7 | 94.7 | 96.5 | 89.3 | 92 | 93.7
100Hz | -69.9 | -70.4 | -70.9 | -73.7 | -74.6 | -75.2 | -77.2 | -81.9 | -94.1 | -95.1 | -95.2 | -86.4 | -79.2 | -78.8 | -79.9 | -81 | -78 | -73.9 | -89.4 | -85.4 | -82
220Hz | -59.2 | -60.5 | -71.6 | -65.8 | -68.2 | -67.1 | -73.7 | -84.6 | -68.4 | -75.8 | -98.5 | -82.4 | -84.2 | -76.1 | -86.3 | -87.4 | -87.1 | -93.72 | -93.2
440Hz | -42.4 | -38 | -40.2 | -37.3 | -28.4 | -28.1 | -29.1 | -33.2 | -45.5 | -81.2 | -74.8 | -45.7 | -58.9 | -52.5 | -69.3 | -72.6 | -65.6 | -68.9 | -69.9 | -85.8 | -94 | -27.3 | -27.6 | -27.2 | -46.1 | -46.6 | -37.1 | -33.2
1000Hz | -52.2 | -53 | -46 | -41.1 | -49.7 | -54.8 | -57 | -58.2 | -51 | -49.3 | -48.7 | -34.1 | -34.9 | -48.7 | -44.4 | -35.8 | -48.4 | -33.8 | -35.7 | -37.4 | -40.2 | -71.6 | -81 | -98 | -74.9 | -85.3 | -89.9 | -78
3200Hz | -20.3 | -18.2 | -18.6 | -18.3 | -21 | -19.2 | -31 | -23.5 | -23 | -21.6 | -22.8 | -24.4 | -19.1 | -18.8 | -29.3 | -34.2 | -33.5 | -58.6 | -39.2 | -52 | -54 | -34.5 | -55 | -45.5 | -37.1 | -44.3
94 dB – frequency response measurement
Each frequency
Different sensitivity
(relative loudness)
Different slope
(change in relative loudness)
Not very optimistic
- For ideal microphone should be one curve

## Slide 34: Why is sound distorted?
Speech – narrow range of frequencies
- sound card will adapt its sensitivity
Song – wide frequency span – great variation in relative loudness – sound card unable to adapt its sensitivity
Microphone can be used only to narrow range of frequencies (speech) – due to its non-linearity
Notes: Jedna frequency potlaci ine to sa neda lebo jedna frequency prehlusi druhu – ona nastavi citlivost na nejaku slabu a ta silna bude tak prehlucnena ze to bude uz prepalene.. Squares nie sinusi

## Slide 35: Directional pattern
L=94dB
f=3200Hz
10°
Relative axes 0 = -60 dB (relative loudness)
Notes: We measured relative sensitivity relative to the sensitivity to the sound produced directly in front of the mic – pattern displays the relative sens. Depending on angle from the front direction and we can see that with increasing angle the magnitude decreases ( it is represented by the distance from origin to the point (radius of imaginary circle)) , there is then again increases when speaker is directly behind the mic --- During the measurement, the angle is different but the distance remains constant (and constant loudness) ------ Pattern similar to standard patterns found on the internet..
Zavisi od hlasitosti a frequency chyba merania.. Dost slbe zvuky

## Slide 36: Conclusion
Explained the principle
Investigated components of microphone
Our own microphone 
Characteristics of microphone
  Frequency response
  Investigated the ‘hole’ effect
  Amplitude response
  - Narrow range
  Direction
Thank you for your attention

## Slide 37: APPENDICES
Thanks to Martin Ferianc for technical support

## Slide 38: Directional – relative magnitude
Chart: Angle [°]
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320 | 330 | 340 | 350 | 360
 | 20 | 19.0624 | 17.6587 | 16.5064 | 15.7495 | 14.3511 | 13.0328 | 10.4495 | 9.7946 | 7.6713 | 6.5685 | 5.1725 | 5.9801 | 3.9808 | 5.7331 | 5.2612 | 6.5305 | 8.5597 | 9.3656 | 8.972 | 6.141 | 5.217 | 4.4289 | 3.9808 | 7.3306 | 6.9034 | 8.5898 | 9.9502 | 10.7827 | 11.3257 | 13.2111 | 15.9321 | 17.8574 | 17.7009 | 19.4583 | 19.7292 | 20

## Slide 39: Carbon Powder
Graphite – is a very bad conductor !
big changes in resistance
Idealy no add. Substances
Van der Waals (170 pm)
Group, period, block
14, 2, p

## Slide 40: Carbon Powder
Stable
Triple point is at
10.8 ± 0.2 MPa
4,600 ± 300 K
Sublimates at 3,900 K.
Carbon powder of the carbon microphone

## Slide 41
Membrane
Chamber with carbon grains
Resistor
Voltage source

## Slide 42: Hi, how are you…?
Factory made
Home made
Factory records speech better – small range of frequencies – what about song?
Notes: Rec je na uzkom range frequencies – podobnu citlivost – pesnicka nie je na uzkom 100 – 1000, slaba citlivost
V nahravke reci vidime ze kvalita zvuku z microphone je lepsia

## Slide 43: Comparison
Home made
R=5000Ω
Factory assembled
R=100Ω
The record of the song with factory made has similar ‘quality’ as with home made – as predicted by its characteristics
Home made
Factory made
Notes: Used our because non stable this was the best we could after many times –granules might be better – from some other electronic device equipment (filter – activated)- not made for this purpose
Home made similar to factrory, due to low - zvukovka z toho robi chaos---