## Slide 1: 14 . Rubber Motor
‘A twisted rubber band stores energy and can be used to power a model aircraft for example. Investigate the properties of such an energy source and how its power output changes with time.’
IYPT 2014
Team Croatia
Reporter: Ilona Benko

## Slide 2: Properties of rubber materials
elastomer  viscoelasticity
Mullins’ effect
  hysteresis while stretching, entire energy isn’t restored, waste in a form of thermal energy
structure coiled molecular chains, polymers (covalent bonds) whose entropy decreases when rubber band is being stretched*
  unstretched rubber band is in the state of maximum entropy
  * I.M. Ward, J. Sweeney: An Introduction to the Machanical Properties of Solid Polymers

## Slide 3: Observation of how does motor work

## Slide 4: Experimental setup
sound card
lamp
photoresistor
ball bearing with gaps
coiled rubber threads
stand
generator
resistor

## Slide 5: Processing measurements
coiling and uncoiling of rubber band recorded in Audacity (.wav)
than reformatted into
.txt files to continue
further processing in
our programs we made for analysis
after processing in those programs, change of angle in time is known and angular velocity, kinetic energy, force and power output can be calculated

## Slide 6: Mathematical model of osilaroty motion
φ – angle [rad]
ω – angular velocity [rad/s]
f – frequency [Hz]
τ – torque [Nm]
k – force constant (for 5 threads =
5,35 *10-5) [Nm/rad]
I - moment of inertia (7,8 * 10-4 )[kgm2]
Ek - kinetic energy[J]
– potential energy[J]
P - power[Watt]
Without friction:
General solution of this equasion for mechanical oscillator is:
is starting phase, and

## Slide 7: Graph: first derivation of angular velocity/time vs angle in radians
0 - line coefficient of proportionality
Measuring 0

## Slide 8: Mathematical model of oscilaroty motion
φ – angle[rad]
ω – angular velocity [rad/s]
f – frequency [Hz]
τ – torque [Nm]
k – force constant (for 5 threads =
5,35 *10-5) [Nm/rad]
I - moment of inertia (7,8 * 10-4 )[kgm2]
Ek - kinetic energy[J]
– potential energy[J]
P - power[Watt]
– friction faktor
Damped oscillations:
General solution of this equasion for mechanical oscillator is:
is starting phase,

## Slide 9: Mathematical model of osilaroty motion
φ – angle[rad]
ω – angular velocity [rad/s]
f – frequency [Hz]
τ – torque [Nm]
k – force constant (for 5 threads =
5,35 *10-5) [Nm/rad]
I - moment of inertia (7,8 * 10-4 )[kgm2]
Ek - kinetic energy[J]
– potential energy[J]
P - power[Watt]
Energy and power:
Ek I ω2
k φ2
P

## Slide 10: Result analysis
bundle of 5 rubber threads
bundle length: 16 cm
nubmer of coils: 61,5
Graph 1: angle vs time

## Slide 11: Result analysis
bundle of 5 rubber threads
bundle length: 16 cm
nubmer of coils: 61,5
Graph 2: anglular velocity vs time

## Slide 12: Result analysis
bundle of 5 rubber threads
bundle length: 16 cm
nubmer of coils: 61,5
Graph 3: energy vs time

## Slide 13: Result analysis
bundle of 5 rubber threads
bundle length: 16 cm
nubmer of coils: 61,5
Graph 4: power vs time

## Slide 14: Analysis of different number of coils
l=18 cm

## Slide 15: Analysis of different number of coils
l=18 cm

## Slide 16: Analysis of different bundle lengths

## Slide 17: Analysis of different bundle lengths

## Slide 18: Analysis of different number of threads

## Slide 19: Analysis of different number of threads

## Slide 20
New setup and measuring torque

## Slide 21
Analysis of different number of threads

## Slide 22: Conclusion
energy which moves the motor comes from kinetic and potential energy stored in molecules of which rubber material is consisted
while in motion, damping slows and finally stops motor
hysteresis  energy loss happens because of heating and friction in oscillatory motion
more power can be gained by:
  using bundle made of maximum number of rubber threads
  using longer bundle
  increasing rubber tension or number of coils
when tension is increased, more energy is gained in exact time interval
hysteresis also rapidly increases as we gain more energy from motor

## Slide 23: Literature list
Hysteresis and Rubber Bands (madphysics.com)
Elastomers and entropic springs (Aparna Baskaran, Syracuse University)
Stretching a Rubber Band (schoolphysics.co.uk)
I. M. Ward and J. Sweeney. An introduction to the mechanical properties of solid polymers (Wiley, 2005)
A. N. Gent. Rubber Elasticity: Basic Concepts and Behavior; Science and Technology of Rubber (Elsevier, 2005)
L. G. McAneny. Rubber band powered motor for model airplane
G. Savarino and M. R. Fisch. A general physics laboratory investigation of the thermodynamics of a rubber band
J. Pellicer, J. A. Manzanares, J. Zúniga, and P. Utrillas. Thermodynamics of rubber elasticity. J. Chem
C. M. Roland. The Mullins effect in crosslinked rubber