## Slide 1: Ball Sound
Jakub Chudík
4

## Slide 2: Task
When two hard steel balls, or similar, are brought gently into contact with each other, an unusual ‘chirping’ sound may be produced.
Investigate and explain the nature of the sound.

## Slide 3: Different Balls
Chosen for the longest duration and
the lowest prevalent frequency
Collisions between different
balls and one large steel ball

## Slide 4: In our presentation
Recreate the sound
Nature of the sound
Examine the sound

## Slide 5: Possible sources
Impulsive translational acceleration
Vibration of the balls

## Slide 6: Vibrations for steel balls of 5cm diam.
Mode number | Natural frequency (kHz)
1 | 51.8
2 | 68.3
3 | 77
4 | 93.1
5 | 97
6 | 98.5
7 | 118.7
8 | 128.2
9 | 136.7
10 | 138.3
Lowest frequency
is 51,8 kHz
K. Mehraby et al. „Impact noise radiated by collision of two spheres“, Journal of Mechanical Science and Technology 25 (7) (2011)
Limit of human ear
is 18-20 kHz
Lowest frequency
for our
balls is 64,75 kHz
Vibrations of the balls certainly
do not contribute to audible sound!

## Slide 7: Impulsive translational acceleration
One oscillating sphere
Two colliding spheres
K. Mehraby et al. „Impact noise radiated by collision of two spheres“, Journal of Mechanical Science and Technology 25 (7) (2011)

## Slide 8: Impulsive translational acceleration
One collision
Two colliding spheres
K. Mehraby et al. „Impact noise radiated by collision of two spheres“, Journal of Mechanical Science and Technology 25 (7) (2011)

## Slide 9
Recreate the sound
Nature of the sound
Examine the sound

## Slide 10: Our apparatus

## Slide 11: Sound analysis
Whole sound made
of individual collisions

## Slide 12: Sound of individual collisions

## Slide 13: Sound of individual collisions
Decreasing amplitude
Individual collisions are similar
But the chirping has a rising tone
Time between collisions
is decreasing

## Slide 14: Spectral analysis of our measured chirping
Time
Frequency

## Slide 15: Spectrum of chirping sound (FFT)
First few collisions: distinguishable
“Fluent” sound

## Slide 16: Spectrum of chirping sound (FFT)
Peaks rising in time

## Slide 17: Time between collisions
Chart: Time [s]

## Slide 18: Frequency of collisions in time
Chart: Time [second]

## Slide 19: Spectrum of chirping sound (FFT)
Pattern is caused by
increase of
frequency of collisions
Peaks rise in time
… if you remember…
Chart: 

## Slide 20
=n*
Chart: 
Chart: 
Frequency of collisions

## Slide 21
=n*
Chart: 
Chart: 
Multiple of frequency
of collisions

## Slide 22
=n*
Chart: 
Chart: 

## Slide 23
=n*
Chart: 
Chart: 

## Slide 24
=n*
Chart: 
Chart: 

## Slide 25
Recreate the sound
Nature of the sound
Examine the sound

## Slide 26: Ingredients for an artificial sound
Time of individual collisions
Impact speed for each collision
  Determines loudness
Sound of a single collision
Chart: Time [s]

## Slide 27: Simplified model of collisions
Constant attractive force
Time between 2 collisions:
mass speed after the last collision
Coefficient of restitution:
Impact speed change:

## Slide 28: Simplified model of collisions
Impact speed decrease in time:
  Suitable for fast chirping
Speed before collisions:
Time between collisions:

## Slide 29: Reality check
Chart: Time [s]
Distortions caused
by hitting the foam

## Slide 30: Reality check
Chart: Time [s]

## Slide 31: Reality check
Chart: Time [s]
Similar to real behavior!

## Slide 32: Notable conclusions
LOUD
LOUD
quiet
quiet
Loudness of the sound
But not
negligible
But not
negligible

## Slide 33: Sound creation in Mathematica

## Slide 34: Artificial vs. Real

## Slide 35: Conclusion – Nature of sound
Two options
  Vibration of balls
  Impulsive translational acceleration
Mode number | Natural frequency (kHz)
1 | 51.8
2 | 68.3
3 | 77
4 | 93.1
5 | 97
6 | 98.5
7 | 118.7
8 | 128.2
9 | 136.7
10 | 138.3
Lowest frequency
of our balls
113,5 kHz

## Slide 36: Conclusion – Analysis and Recreation
Simplified model of collision
Advanced theory
  L. L. Koss, R. J. Alfredson:
Generated authentic sound
Chart: Time [s]

## Slide 37
=n*
Chart: 
Thank you for
your attention

## Slide 38: Sound of single collision
K. Mehraby et al:
“Impact noise radiated by collision of two spheres“ Journal of Mechanical Science and Technology, 2011
L. L. Koss, R. J. Alfredson:
“Transient sound radiated by spheres undergoing an elastic collision” Journal of Sound and Vibration, 1972
  Fully theoretical & analytical
  solution
  Underestimates the loudness
  for theta=90°
  Otherwise good correlation
  Finite elements method simulation
  “Perfect” agreement with experiment

## Slide 39: Koss & Alfredson: Theory basis
Fourier transform of ball’s motion
Velocity potential for colliding balls
Interaction of balls:
  Acceleration approximation:
Velocity potential for an oscillating sphere*:
*I. Malecki: Physical Foundations of Technical Acoustics
(duration of contact)

## Slide 40: Koss & Alfredson: results

## Slide 43
Chart: Frequency of collisions in time

## Slide 44: Different Balls
No principial difference in sound
Sound differs in frequency and duration
6200 Hz
7000 Hz
8000 Hz
7700 Hz
5000 Hz

## Slide 45: Sound analysis

## Slide 46: Procedure of Fourier transform
Scanned area
FFT size

## Slide 47
Chart: Frequency of collisions in time

## Slide 48: Period of collisions
Chart: Time [s]
Similar to real behavior!!

## Slide 49
If all collisions are the same
only frequency of the
collisions increases
we can generate sound

## Slide 50: Generating fake chirping sound
Take 1 collision
And decreasing amplitude
Paste 185 times with increasing frequency

## Slide 51: Reality check
Generated
Measured

## Slide 52: Single collision – our measurement vs theory

## Slide 53: Spectral analysis
Distinguish individual collisions
Pattern caused by increasing frequency of the collisions

## Slide 54: Our apparatus
Steel Balls:
Radius: 1.43 cm
Mass: 0.095 kg
Colliding on soft foam
Little energy losses due to damping

## Slide 55: Single collision noise approximation
Chart: 
Real waveform

## Slide 56: Chirping sound
Subsequent Identical sounds
Chart: 
REAL chirping sound

## Slide 57: Second verification method
We can generate chirping sound by pasting the same single-collision-waveform one after another

## Slide 58
Now we know the motion of the balls
Chart: Time [second]
Chart: Time [s]

## Slide 59
Motion
Origin
Why do we hear the chirping?

## Slide 60: Spectrum of one collision
Fourier transform
Our model
Let’s put the collisions together!

## Slide 61: Spectrum of one moment of chirping
200Hz – frequency of collisions

## Slide 62
Peak in time rising
Time is increasing => frequency of collisions increasing