## Slide 1: Coefficient of diffusion
Marek Bašista
10

## Slide 2: Assignment
Using a microscope, observe the Brownian motion of a particle of the order of micrometer in size. Investigate how the coefficient of diffusion depends on the size and shape of the particle.

## Slide 3: Observation
Carbon particles in water

## Slide 4: What is the Brownian motion
X
Y
Particle moves = diffunds

## Slide 5: What is the Brownian motion? Simulation 2D
Source: http://www.rpgroup.caltech.edu/courses/aph162/2006/Protocols/diffusion.pdf

## Slide 6: Diffusion equation in 2D
P
x
y
Source: http://www.rpgroup.caltech.edu/courses/aph162/2006/Protocols/diffusion.pdf
Solution (1. time used Fourier transformation):

## Slide 7: Diffusion equation in 2D
Position [x(t), y(t)] cannot be predicted but and can.
Logically:
Using polar coordinates:
The most probable position is [0, 0] - initial state
Source: http://www.rpgroup.caltech.edu/courses/aph162/2006/Protocols/diffusion.pdf
Dt
Generally for n dimensions:

## Slide 8: Coefficient of diffusion
Calculation by Einstein (1905):
– for spheres (Stokes)
– dynamic viscosity of the fluid
d
k - Boltzmann constant
T - thermodynamic temperature
d – diameter of the particle

## Slide 9: How to measure D(d)?
Choose small time interval t (time between frames).
Determine square of particle displacement during t.
Repeat steps 1. and 2. as many times as possible.
Calculate average value of r² - .
Calculate D.
D=
r
Time 0s
Time t

## Slide 10: Experiments
10

## Slide 11: Experimental equipment

## Slide 12: Our tried particles
POLYMERS AND TiO2
LATEX PAINT
CARBON PARTICLES
CARBON - INDIAN INK

## Slide 13: Callibration of the size
Burker's chamber – used for red blood cells calculation, 50µm*50µm raster

## Slide 14: Particle size measurement problem? Diffraction of light
-Apparent size of particle is about 2λ larger than real one
-Substraction of 2λ is unusable for small particles (less than 1µm)
Airy disc – small point source image
~3,3 µm
~2,2 µm

## Slide 15: Position vector square (time)
OBR cely screen 1.SG
Milk fat particle – analysis

## Slide 16: Experiment 1: Radii determination
10

## Slide 17: Probability distribution function – effective radii determination
X/Y displacement during constant time ~ 66ms
MILK FAT PARTICLES
Chart: Displacement [µm]
| -1.2956269278599994 | -1.1722338871114277 | -1.0488408463628565 | -0.92544780561428519 | -0.8020547648657137 | -0.67866172411714243 | -0.55526868336857116 | -0.43187564261999972 | -0.3084826018714284 | -0.18508956112285702 | -6.1696520374285677E-2 | 6.1696520374285677E-2 | 0.18508956112285702 | 0.3084826018714284 | 0.43187564261999972 | 0.55526868336857116 | 0.67866172411714243 | 0.8020547648657137 | 0.92544780561428519 | 1.0488408463628565 | 1.1722338871114277
Y Direction | 0.00062073 | 0.00062073 | 0.0031037 | 0.009311 | 0.011794 | 0.027933 | 0.049038 | 0.064556 | 0.092489 | 0.12477 | 0.14215 | 0.14277 | 0.11235 | 0.087523 | 0.063315 | 0.036002 | 0.015518 | 0.0080695 | 0.0062073 | 0.0012415 | 0.00062073
Y Direction fit | 0.00015503 | 0.00053297 | 0.0016194 | 0.0043491 | 0.010323 | 0.021656 | 0.040153 | 0.065802 | 0.095308 | 0.12201 | 0.13804 | 0.13804 | 0.12201 | 0.095308 | 0.065802 | 0.040153 | 0.021656 | 0.010323 | 0.0043491 | 0.0016194 | 0.00053297
Chart: Displacement [µm]
| -1.2956269278599994 | -1.1722338871114277 | -1.0488408463628565 | -0.92544780561428519 | -0.8020547648657137 | -0.67866172411714243 | -0.55526868336857116 | -0.43187564261999972 | -0.3084826018714284 | -0.18508956112285702 | -6.1696520374285677E-2 | 6.1696520374285677E-2 | 0.18508956112285702 | 0.3084826018714284 | 0.43187564261999972 | 0.55526868336857116 | 0.67866172411714243 | 0.8020547648657137 | 0.92544780561428519 | 1.0488408463628565 | 1.1722338871114277
Y Direction | 0.00062073 | 0.00062073 | 0.0031037 | 0.009311 | 0.011794 | 0.027933 | 0.049038 | 0.064556 | 0.092489 | 0.12477 | 0.14215 | 0.14277 | 0.11235 | 0.087523 | 0.063315 | 0.036002 | 0.015518 | 0.0080695 | 0.0062073 | 0.0012415 | 0.00062073
Y Direction fit | 0.00015503 | 0.00053297 | 0.0016194 | 0.0043491 | 0.010323 | 0.021656 | 0.040153 | 0.065802 | 0.095308 | 0.12201 | 0.13804 | 0.13804 | 0.12201 | 0.095308 | 0.065802 | 0.040153 | 0.021656 | 0.010323 | 0.0043491 | 0.0016194 | 0.00053297
Chart: Displacement [µm]
| -1.6088757906000006 | -1.4556495248285721 | -1.3024232590571434 | -1.1491969932857149 | -0.99597072751428617 | -0.84274446174285755 | -0.68951819597142894 | -0.53629193020000021 | -0.3830656644285716 | -0.22983939865714298 | -7.6613132885714322E-2 | 7.6613132885714322E-2 | 0.22983939865714298 | 0.3830656644285716 | 0.53629193020000021 | 0.68951819597142894 | 0.84274446174285755 | 0.99597072751428617 | 1.1491969932857149 | 1.3024232590571434 | 1.4556495248285721
X Direction | 0.001243 | 0.0018645 | 0.002486 | 0.0055935 | 0.0087011 | 0.017402 | 0.027346 | 0.042884 | 0.088254 | 0.12244 | 0.15165 | 0.15351 | 0.13611 | 0.10255 | 0.065879 | 0.038533 | 0.01243 | 0.011809 | 0.004972 | 0.0031075 | 0.001243
X Direction fit | 3.4797e-05 | 0.0001599 | 0.00063087 | 0.0021369 | 0.0062146 | 0.015517 | 0.033263 | 0.061219 | 0.096733 | 0.13123 | 0.15285 | 0.15285 | 0.13123 | 0.096733 | 0.061219 | 0.033263 | 0.015517 | 0.0062146 | 0.0021369 | 0.00063087 | 0.0001599
Chart: Displacement [µm]
| -1.6088757906000006 | -1.4556495248285721 | -1.3024232590571434 | -1.1491969932857149 | -0.99597072751428617 | -0.84274446174285755 | -0.68951819597142894 | -0.53629193020000021 | -0.3830656644285716 | -0.22983939865714298 | -7.6613132885714322E-2 | 7.6613132885714322E-2 | 0.22983939865714298 | 0.3830656644285716 | 0.53629193020000021 | 0.68951819597142894 | 0.84274446174285755 | 0.99597072751428617 | 1.1491969932857149 | 1.3024232590571434 | 1.4556495248285721
X Direction | 0.001243 | 0.0018645 | 0.002486 | 0.0055935 | 0.0087011 | 0.017402 | 0.027346 | 0.042884 | 0.088254 | 0.12244 | 0.15165 | 0.15351 | 0.13611 | 0.10255 | 0.065879 | 0.038533 | 0.01243 | 0.011809 | 0.004972 | 0.0031075 | 0.001243
X Direction fit | 3.4797e-05 | 0.0001599 | 0.00063087 | 0.0021369 | 0.0062146 | 0.015517 | 0.033263 | 0.061219 | 0.096733 | 0.13123 | 0.15285 | 0.15285 | 0.13123 | 0.096733 | 0.061219 | 0.033263 | 0.015517 | 0.0062146 | 0.0021369 | 0.00063087 | 0.0001599
Nearly spherical particle »

## Slide 18: Experiment 2: Particle Size
10

## Slide 19: Observation - explanation
100 µm
Particles in latex paint, diluted in distilled water for lowering concentration.

## Slide 20: Particle size
Chart: Particle diameter d [µm]
| 0.67 | 0.97000000000000008 | 1.5699999999999998 | 2.57 | 3.4699999999999998 | 4.7699999999999996
 | 6.9474 | 5.6825 | 3.5595 | 1.762 | 2.2288 | 0.4701
 | 7.478 | 5.1652 | 3.1913 | 1.9495 | 1.4439 | 1.0504
fit
Big particle - collisions with glass » reduced diffusion coefficient

## Slide 21: Experiment 3: Particle Shape
10

## Slide 22: Influence on the diffusion
Diffusion is similar as for spherical particles - prolonged particle rotates randomly
Average behavior is like as for spherical particle with some effective radius

## Slide 23: X-Y position analysis
Graf 1, 2
Rx approx Ry approx 1,02 um
? Like a spherical particle?
Particles rotates during the diffusion
Average behavior as spherical particle (for long observation time)
Chart: 
| -0.43613262050000001 | -0.35683578040909092 | -0.27753894031818183 | -0.19824210022727273 | -0.11894526013636364 | -3.9648420045454547E-2 | 3.9648420045454547E-2 | 0.11894526013636364 | 0.19824210022727273 | 0.27753894031818183 | 0.35683578040909092 | -0.39805340250000015 | -0.32568005659090921 | -0.25330671068181826 | -0.18093336477272731 | -0.10856001886363639 | -3.6186672954545467E-2 | 3.6186672954545467E-2 | 0.10856001886363639 | 0.18093336477272731 | 0.25330671068181826 | 0.32568005659090921 | -0.45 | -0.42499999999999999 | -0.4 | -0.375 | -0.35 | -0.32500000000000001 | -0.3 | -0.27500000000000002 | -0.25 | -0.22500000000000001 | -0.2 | -0.17499999999999999 | -0.15 | -0.125 | -0.1 | -7.4999999999999997E-2 | -0.05 | -2.5000000000000001E-2 | 0 | 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125000000000001 | 0.15000000000000099 | 0.17500000000000099 | 0.20000000000000101 | 0.225000000000001 | 0.250000000000001 | 0.27500000000000102 | 0.30000000000000099 | 0.32500000000000101 | 0.35000000000000098 | 0.375000000000001 | 0.40000000000000102 | 0.42500000000000099 | 0.45000000000000101
X Direction | 0.016216 | 0.010811 | 0.043243 | 0.097297 | 0.19459 | 0.21622 | 0.2 | 0.13514 | 0.048649 | 0.010811 | 0.027027
Y Direction | 0 | 0.037838 | 0.043243 | 0.1027 | 0.12432 | 0.24324 | 0.18919 | 0.10811 | 0.10811 | 0.032432 | 0.010811
X Direction fit | 0.0014686 | 0.0025264 | 0.0042135 | 0.0068127 | 0.010679 | 0.016229 | 0.023909 | 0.03415 | 0.047288 | 0.063482 | 0.082621 | 0.10425 | 0.12752 | 0.15122 | 0.17386 | 0.19379 | 0.2094 | 0.21937 | 0.22279 | 0.21937 | 0.2094 | 0.19379 | 0.17386 | 0.15122 | 0.12752 | 0.10425 | 0.082621 | 0.063482 | 0.047288 | 0.03415 | 0.023909 | 0.016229 | 0.010679 | 0.0068127 | 0.0042135 | 0.0025264 | 0.0014686
Y Direction fit | 0.0006424 | 0.0012062 | 0.0021848 | 0.0038172 | 0.0064337 | 0.01046 | 0.016405 | 0.024819 | 0.03622 | 0.05099 | 0.069244 | 0.090708 | 0.11462 | 0.13972 | 0.1643 | 0.18636 | 0.20391 | 0.21522 | 0.21913 | 0.21522 | 0.20391 | 0.18636 | 0.1643 | 0.13972 | 0.11462 | 0.090708 | 0.069244 | 0.05099 | 0.03622 | 0.024819 | 0.016405 | 0.01046 | 0.0064337 | 0.0038172 | 0.0021848 | 0.0012062 | 0.0006424
Particle rotates – average behavior as a spherical particle (for long observation time)
Probability
Displacement [µm]

## Slide 24: But – change of coordinate system makes difference!
L
T
x
y
We will analyse the motion of the particle ALONG and PERPENDICULARY to its main axis
We set NEW coordinate system for each individual time step in the center of the particle.

## Slide 25: Longitudinal and Transversal movement
Particle moves more in transversal direction than longitudinal
Probability
Displacement[µm]
Chart: 
| -0.43613262050000001 | -0.35683578040909092 | -0.27753894031818183 | -0.19824210022727273 | -0.11894526013636364 | -3.9648420045454547E-2 | 4.2316717650685842E-2 | 0.12161355774159494 | 0.19824210022727273 | 0.27753894031818183 | 0.35683578040909092 | -0.39805340250000015 | -0.32568005659090921 | -0.25330671068181826 | -0.18093336477272731 | -0.10856001886363639 | -3.6186672954545467E-2 | 4.0438223670883559E-2 | 0.11281156957997449 | 0.18093336477272731 | 0.25330671068181826 | 0.32568005659090921 | -0.45 | -0.42499999999999999 | -0.4 | -0.375 | -0.35 | -0.32500000000000001 | -0.3 | -0.27500000000000002 | -0.25 | -0.22500000000000001 | -0.2 | -0.17499999999999999 | -0.15 | -0.125 | -0.1 | -7.4999999999999997E-2 | -0.05 | -2.5000000000000001E-2 | 0 | 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125000000000001 | 0.15000000000000099 | 0.17500000000000099 | 0.20000000000000101 | 0.225000000000001 | 0.250000000000001 | 0.27500000000000102 | 0.30000000000000099 | 0.32500000000000101 | 0.35000000000000098 | 0.375000000000001 | 0.40000000000000102 | 0.42500000000000099 | 0.45000000000000101
Longitudinal Direction | 0.016129 | 0.0053763 | 0.037634 | 0.053763 | 0.13441 | 0.25269 | 0.25806 | 0.12366 | 0.091398 | 0.016129 | 0.010753
Transversal Direction | 0.021739 | 0.027174 | 0.059783 | 0.10326 | 0.15761 | 0.21196 | 0.20109 | 0.10326 | 0.076087 | 0.027174 | 0.01087
Longitudinal Direction fit | 0.00047392 | 0.00093944 | 0.0017908 | 0.0032829 | 0.0057873 | 0.0098111 | 0.015995 | 0.025076 | 0.037806 | 0.054812 | 0.076421 | 0.10246 | 0.13211 | 0.16381 | 0.19532 | 0.22397 | 0.24697 | 0.26188 | 0.26705 | 0.26188 | 0.24697 | 0.22397 | 0.19532 | 0.16381 | 0.13211 | 0.10246 | 0.076421 | 0.054812 | 0.037806 | 0.025076 | 0.015995 | 0.0098111 | 0.0057873 | 0.0032829 | 0.0017908 | 0.00093944 | 0.00047392
Transversal direction fit | 0.0035201 | 0.0054587 | 0.0082553 | 0.012176 | 0.017513 | 0.024567 | 0.033609 | 0.044839 | 0.058342 | 0.074031 | 0.091614 | 0.11057 | 0.13013 | 0.14937 | 0.16721 | 0.18255 | 0.19435 | 0.2018 | 0.20435 | 0.2018 | 0.19435 | 0.18255 | 0.16721 | 0.14937 | 0.13013 | 0.11057 | 0.091614 | 0.074031 | 0.058342 | 0.044839 | 0.033609 | 0.024567 | 0.017513 | 0.012176 | 0.0082553 | 0.0054587 | 0.0035201
Transversal Direction fit

## Slide 26: Explanation
a
l

## Slide 27: Conclusion
Observation of the Brownian motion (latex paint, milk, carbon particles)
Theory – Diffusion equation
P
x
y
Analysis of diffusion movement of spherical particle – determination of effective radii and
Chart: Probability
| -1.2956269278599994 | -1.1722338871114277 | -1.0488408463628565 | -0.92544780561428519 | -0.8020547648657137 | -0.67866172411714243 | -0.55526868336857116 | -0.43187564261999972 | -0.3084826018714284 | -0.18508956112285702 | -6.1696520374285677E-2 | 6.1696520374285677E-2 | 0.18508956112285702 | 0.3084826018714284 | 0.43187564261999972 | 0.55526868336857116 | 0.67866172411714243 | 0.8020547648657137 | 0.92544780561428519 | 1.0488408463628565 | 1.1722338871114277
Y Direction | 0.00062073 | 0.00062073 | 0.0031037 | 0.009311 | 0.011794 | 0.027933 | 0.049038 | 0.064556 | 0.092489 | 0.12477 | 0.14215 | 0.14277 | 0.11235 | 0.087523 | 0.063315 | 0.036002 | 0.015518 | 0.0080695 | 0.0062073 | 0.0012415 | 0.00062073
Y Direction fit | 0.00015503 | 0.00053297 | 0.0016194 | 0.0043491 | 0.010323 | 0.021656 | 0.040153 | 0.065802 | 0.095308 | 0.12201 | 0.13804 | 0.13804 | 0.12201 | 0.095308 | 0.065802 | 0.040153 | 0.021656 | 0.010323 | 0.0043491 | 0.0016194 | 0.00053297
Chart: Probability
| -1.2956269278599994 | -1.1722338871114277 | -1.0488408463628565 | -0.92544780561428519 | -0.8020547648657137 | -0.67866172411714243 | -0.55526868336857116 | -0.43187564261999972 | -0.3084826018714284 | -0.18508956112285702 | -6.1696520374285677E-2 | 6.1696520374285677E-2 | 0.18508956112285702 | 0.3084826018714284 | 0.43187564261999972 | 0.55526868336857116 | 0.67866172411714243 | 0.8020547648657137 | 0.92544780561428519 | 1.0488408463628565 | 1.1722338871114277
Y Direction | 0.00062073 | 0.00062073 | 0.0031037 | 0.009311 | 0.011794 | 0.027933 | 0.049038 | 0.064556 | 0.092489 | 0.12477 | 0.14215 | 0.14277 | 0.11235 | 0.087523 | 0.063315 | 0.036002 | 0.015518 | 0.0080695 | 0.0062073 | 0.0012415 | 0.00062073
Y Direction fit | 0.00015503 | 0.00053297 | 0.0016194 | 0.0043491 | 0.010323 | 0.021656 | 0.040153 | 0.065802 | 0.095308 | 0.12201 | 0.13804 | 0.13804 | 0.12201 | 0.095308 | 0.065802 | 0.040153 | 0.021656 | 0.010323 | 0.0043491 | 0.0016194 | 0.00053297
Chart: Probability
| -1.6088757906000006 | -1.4556495248285721 | -1.3024232590571434 | -1.1491969932857149 | -0.99597072751428617 | -0.84274446174285755 | -0.68951819597142894 | -0.53629193020000021 | -0.3830656644285716 | -0.22983939865714298 | -7.6613132885714322E-2 | 7.6613132885714322E-2 | 0.22983939865714298 | 0.3830656644285716 | 0.53629193020000021 | 0.68951819597142894 | 0.84274446174285755 | 0.99597072751428617 | 1.1491969932857149 | 1.3024232590571434 | 1.4556495248285721
X Direction | 0.001243 | 0.0018645 | 0.002486 | 0.0055935 | 0.0087011 | 0.017402 | 0.027346 | 0.042884 | 0.088254 | 0.12244 | 0.15165 | 0.15351 | 0.13611 | 0.10255 | 0.065879 | 0.038533 | 0.01243 | 0.011809 | 0.004972 | 0.0031075 | 0.001243
X Direction fit | 3.4797e-05 | 0.0001599 | 0.00063087 | 0.0021369 | 0.0062146 | 0.015517 | 0.033263 | 0.061219 | 0.096733 | 0.13123 | 0.15285 | 0.15285 | 0.13123 | 0.096733 | 0.061219 | 0.033263 | 0.015517 | 0.0062146 | 0.0021369 | 0.00063087 | 0.0001599
Chart: Probability
| -1.6088757906000006 | -1.4556495248285721 | -1.3024232590571434 | -1.1491969932857149 | -0.99597072751428617 | -0.84274446174285755 | -0.68951819597142894 | -0.53629193020000021 | -0.3830656644285716 | -0.22983939865714298 | -7.6613132885714322E-2 | 7.6613132885714322E-2 | 0.22983939865714298 | 0.3830656644285716 | 0.53629193020000021 | 0.68951819597142894 | 0.84274446174285755 | 0.99597072751428617 | 1.1491969932857149 | 1.3024232590571434 | 1.4556495248285721
X Direction | 0.001243 | 0.0018645 | 0.002486 | 0.0055935 | 0.0087011 | 0.017402 | 0.027346 | 0.042884 | 0.088254 | 0.12244 | 0.15165 | 0.15351 | 0.13611 | 0.10255 | 0.065879 | 0.038533 | 0.01243 | 0.011809 | 0.004972 | 0.0031075 | 0.001243
X Direction fit | 3.4797e-05 | 0.0001599 | 0.00063087 | 0.0021369 | 0.0062146 | 0.015517 | 0.033263 | 0.061219 | 0.096733 | 0.13123 | 0.15285 | 0.15285 | 0.13123 | 0.096733 | 0.061219 | 0.033263 | 0.015517 | 0.0062146 | 0.0021369 | 0.00063087 | 0.0001599

## Slide 28: Conclusion
Measurement of diffusion coefficient in dependence on particle radius – theory – confirmed
Chart: Particle diameter d [µm]
| 0.67 | 0.97000000000000008 | 1.5699999999999998 | 2.57 | 3.4699999999999998 | 4.7699999999999996
 | 6.9474 | 5.6825 | 3.5595 | 1.762 | 2.2288 | 0.4701
 | 7.478 | 5.1652 | 3.1913 | 1.9495 | 1.4439 | 1.0504
Chart: Particle diameter d [µm]
| 0.67 | 0.97000000000000008 | 1.5699999999999998 | 2.57 | 3.4699999999999998 | 4.7699999999999996
 | 6.9474 | 5.6825 | 3.5595 | 1.762 | 2.2288 | 0.4701
 | 7.478 | 5.1652 | 3.1913 | 1.9495 | 1.4439 | 1.0504
fit
Big particle - collisions with glass » reduced diffusion coefficient
Analysis of diffusion movement of strongly aspherical particle
  Behaves like spherical particle in a laboratory frame –
  Asphericity detected from analysis of the longitudinal and transversal movement
Thank you for your attention!

## Slide 29
Carbon particles in water
ENJOY!

## Slide 30: Appendix
10

## Slide 31: Probability distribution function in 1D

## Slide 32: Perrin formulas – drag coefficients
b
a
a
b
c
PROLATE ELLIPSOID
LONG ROD

## Slide 33
b
a
c
OBLATE ELLIPSOID

## Slide 34: Changing coordinate system! - equations
L
T
x
y

## Slide 35: Mass of the particle
Type equation here.
t-time between collisions - ~10(-8)s