## Slide 1: Pot-in-Pot refridgerator
Natália Ružičková
7

## Slide 2: Task
The ‘pot-in-pot refrigerator’ is a device that keeps food cool using the principle of evaporative cooling.
It consists of a pot placed inside a bigger pot with the space between them filled with a wet porous material, e.g. sand.
How might one achieve the best cooling effect?
Low temperature
Fast cooling

## Slide 3: Mechanism
Wet porous material: Evaporation  latent heat  cooling
Heat transfer from the environment
Equillibrium:

## Slide 4: Preliminary Experiment
Porous material: sand
Chart: Time [min]
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110
fridge | 20.1 | 20.2 | 20.1 | 19.9 | 19.9 | 19.7 | 19.7 | 19.6 | 19.6 | 19.6 | 19.5 | 19.6 | 19.6 | 19.6 | 19.6 | 19.7 | 19.8 | 19.7 | 19.8 | 19.7 | 19.8 | 19.8 | 19.9
enviroment | 20.7 | 20.2 | 20.3 | 20.6 | 20.7 | 20.7 | 20.8 | 20.8 | 20.9 | 20.9 | 21 | 21 | 21.1 | 21.2 | 21.3 | 21.2 | 21.2 | 21.1 | 21.2 | 21 | 20.7 | 20.6 | 20.6
Works, but could be better

## Slide 5: Evaporation requirements
Must be wet (capillarity)
Exposed to air flow

## Slide 6: Sand: a granular material
Big granules:
 Better airflow
 Water drains down
Small granules:
 Can soak with water
 Little space for airflow

## Slide 7: Other kind of porous material: Cloth
Gets soaked with water
Can be exposed to air flow on sufficient area

## Slide 8: Cloth vs. sand: the difference
Chart: Time [min]
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110
cloth + sand | 19.7 | 19.4 | 18.9 | 18.3 | 17.9 | 17.7 | 17.6 | 17.2 | 16.9 | 16.8 | 16.7 | 16.5 | 16.4 | 16.4 | 16.3 | 16.3 | 16.2 | 16.2 | 16 | 16 | 15.9 | 15.9 | 15.9
sand | 20.1 | 20.2 | 20.1 | 19.9 | 19.9 | 19.7 | 19.7 | 19.6 | 19.6 | 19.6 | 19.5 | 19.6 | 19.6 | 19.6 | 19.6 | 19.7 | 19.8 | 19.7 | 19.8 | 19.7 | 19.8 | 19.8 | 19.9
enviroment | 20.7 | 20.2 | 20.3 | 20.6 | 20.7 | 20.7 | 20.8 | 20.8 | 20.9 | 20.9 | 21 | 21 | 21.1 | 21.2 | 21.3 | 21.2 | 21.2 | 21.1 | 21.2 | 21 | 20.7 | 20.6 | 20.6
We have a working refrigerator

## Slide 9: A working refrigerator
Inner pot
Outer pot
Porous material: cloth
Liquid (water) for evaporation
Content
Airflow

## Slide 10: Task
“How might one achieve the best cooling effect?”
Simple model of the cooling
Experimentally verify & optimize
Estimate the best possible cooling
Low temperature
Fast cooling

## Slide 11: Model of the cooling

## Slide 12: Model of the cooling effect
Evaporation rate: related to volatility of the liquid (in air)
Heat transferred from the surroundings: related to thermal conductivity, capacity of air
Surface area
Air flow speed
Temperature difference

## Slide 13: Model of the cooling
Calorimetry:
Final temperature drop:
  Speed of cooling:

## Slide 14: Experimental verification & investigation

## Slide 15: 1. High vs. low outer pot
Terminal temperature:
depends on materials only  Equal
Cooling rate:
more water  bigger  slower cooling

## Slide 16: High vs. low pot: final temperature
Chart: Time[min]
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 65 | 75
With outside pot | 17.9 | 17.7 | 17.7 | 17.4 | 17.3 | 17.2 | 17.1 | 17 | 16.9 | 16.8 | 16.8 | 16.8 | 16.5 | 16.5
Without outside pot | 19.6 | 19.1 | 18.6 | 18.2 | 17.8 | 17.6 | 17.4 | 17.3 | 17.2 | 17 | 17 | 16.9 | 16.7 | 16.6
Environment | 20.9 | 20.9 | 20.9 | 20.9 | 21 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21.1 | 21
Both models:
the same terminal temperature

## Slide 17: High vs. low pot: rate of cooling
Chart: time [s]
Low outer pot:
Less water  smaller thermal capacity  faster cooling

## Slide 18: 2. Size and shape of the fridge
Terminal temperature:
Independent of size/shape
Speed of cooling:
Independent of size/shape
Empty refrigerator: Proportional to surface area

## Slide 19: Effect of different sizes

## Slide 20: Effect of different size
Chart: Different sizes
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Environment | 21.1833 | 21.4833 | 21.1833 | 21.1833 | 21.4833 | 21.3833 | 21.3833 | 21.5833 | 21.5833 | 21.3833 | 21.5833 | 21.5833 | 21.4833 | 21.4833 | 21.2833 | 21.2833 | 21.1833 | 21.2833 | 21.2833 | 21.2833 | 21.3833
Radius 9,5 | 21.2833 | 17.0833 | 14.8833 | 14.3833 | 14.3833 | 14.4833 | 14.1833 | 13.9833 | 13.9833 | 14.0833 | 14.0833 | 13.9833 | 13.9833 | 13.9833 | 13.9833 | 13.8833 | 13.8833 | 13.8833 | 13.8833 | 13.8833 | 13.9833
Radius 7 | 21.0833 | 16.5833 | 15.5833 | 14.7833 | 14.5833 | 14.1833 | 14.1833 | 14.0833 | 13.7833 | 13.7833 | 13.7833 | 13.7833 | 13.8833 | 13.8833 | 13.8833 | 13.8833 | 13.7833 | 13.7833 | 13.6833 | 13.6833 | 13.7833
Radius 6 | 17.6833 | 15.4833 | 15.0833 | 14.6833 | 14.1833 | 13.8833 | 14.1833 | 14.0833 | 14.0833 | 13.9833 | 13.8833 | 13.7833 | 13.7833 | 13.7833 | 13.6833 | 13.6833 | 13.6833 | 13.6833 | 13.5833 | 13.6833 | 13.6833
Radius 4 | 19.6833 | 16.2833 | 14.9833 | 14.3833 | 14.2833 | 14.4833 | 14.0833 | 13.6833 | 13.8833 | 13.7833 | 13.7833 | 13.6833 | 13.6833 | 13.4833 | 13.3833 | 13.3833 | 13.3833 | 13.3833 | 13.3833 | 13.3833 | 13.3833
Radius 3,3 | 19.0833 | 16.5833 | 15.1833 | 14.6833 | 14.3833 | 14.1833 | 14.0833 | 14.0833 | 13.9833 | 13.8833 | 13.7833 | 13.7833 | 13.6833 | 13.5833 | 13.5833 | 13.5833 | 13.5833 | 13.5833 | 13.5833 | 13.5833 | 13.5833

## Slide 21: Effect of different shapes
Chart: Time[min]
| 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 29 | 34 | 39 | 44 | 49 | 54 | 59 | 64 | 69 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 170 | 190 | 210 | 230 | 250
Environment | 21.18 | 18.38 | 16.48 | 15.78 | 15.38 | 15.08 | 14.88 | 14.78 | 14.78 | 14.58 | 14.48 | 14.38 | 14.38 | 14.28 | 14.28 | 14.28 | 13.98 | 13.98 | 13.88 | 13.88 | 13.88 | 13.88 | 13.98 | 13.98 | 13.88 | 13.88 | 13.98 | 13.88 | 13.98 | 14.08 | 14.18
Round | 21.18 | 18.38 | 16.48 | 15.78 | 15.38 | 15.08 | 14.88 | 14.78 | 14.78 | 14.58 | 14.48 | 14.38 | 14.38 | 14.28 | 14.28 | 14.28 | 13.98 | 13.98 | 13.88 | 13.88 | 13.88 | 13.88 | 13.98 | 13.98 | 13.88 | 13.88 | 13.98 | 13.88 | 13.98 | 14.08 | 14.18
Elongated | 21.18 | 19.58 | 15.68 | 14.38 | 13.98 | 12.88 | 13.78 | 13.78 | 13.78 | 13.78 | 13.78 | 13.78 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.68 | 13.58 | 13.58 | 13.78 | 13.88 | 13.78 | 13.78 | 13.78 | 13.88
Elongated - bigger | 21.08 | 19.78 | 18.38 | 17.88 | 17.78 | 15.28 | 14.48 | 14.18 | 14.18 | 14.18 | 14.08 | 14.08 | 14.08 | 13.98 | 13.98 | 14.08 | 14.08 | 14.18 | 13.88 | 13.88 | 13.88 | 13.88 | 14.08 | 13.98 | 13.98 | 13.98 | 13.98 | 13.88 | 14.18 | 14.18 | 14.38
Size and shape of an empty fridge:
No effect on cooling

## Slide 22: 3. What’s inside
Terminal temperature:
Independent of content
Speed of cooling:
High capacity  slower cooling

## Slide 23: Changing heat capacity of the fridge
Chart: Time[min]
| 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 29 | 34 | 39 | 44 | 49 | 54 | 59 | 64 | 69 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 170 | 190 | 210 | 230 | 250
Environment | 21.7 | 21.7 | 21.7 | 22.2 | 22 | 21.9 | 21.8 | 21.8 | 21.8 | 21.8 | 21.8 | 21.4 | 21.3 | 21.4 | 21.3 | 21.4 | 21.3 | 21.3 | 21.4 | 21.7 | 21.3 | 21.7 | 21.4 | 21.3 | 21.2 | 21.2 | 21.2 | 21.1 | 21.2 | 21.3 | 21.3
With air | 21.18 | 18.38 | 16.48 | 15.78 | 15.38 | 15.08 | 14.88 | 14.78 | 14.78 | 14.58 | 14.48 | 14.38 | 14.38 | 14.28 | 14.28 | 14.28 | 13.98 | 13.98 | 13.88 | 13.88 | 13.88 | 13.88 | 13.98 | 13.98 | 13.88 | 13.88 | 13.98 | 13.88 | 13.98 | 14.08 | 14.18
With water | 20.28 | 20.18 | 19.58 | 19.18 | 18.68 | 18.28 | 18.08 | 18.08 | 17.38 | 17.08 | 16.68 | 16.28 | 16.08 | 15.78 | 15.68 | 15.38 | 15.28 | 15.18 | 14.98 | 14.78 | 14.58 | 14.58 | 14.48 | 14.38 | 14.28 | 14.28 | 14.28 | 14.18 | 14.18 | 14.28 | 14.28
With sand | 22.58 | 22.58 | 22.18 | 21.58 | 21.18 | 19.98 | 19.28 | 18.68 | 18.48 | 17.28 | 16.78 | 16.18 | 15.78 | 15.58 | 15.18 | 14.88 | 14.78 | 14.68 | 14.28 | 14.18 | 14.08 | 13.98 | 13.98 | 13.78 | 13.78 | 13.78 | 13.68 | 13.68 | 13.68 | 13.68 | 13.78
Air, quicker cooling
Sand, slower cooling
Water, slowest cooling
Bigger capacity  slower cooling
No effect on final temperature

## Slide 24: 4. Different liquid
Terminal temperature:
Grows with volatility & latent heat
Speed of cooling:
Independent of liquid (only a small capacity difference)

## Slide 25: Water VS. Etanol:
Chart: time [s]
More volatile liquid  lower terminal temperature

## Slide 26: Water vs. ethanol: exponential fit
Water
Ethanol
Different liquids  similar speed of cooling
Slight difference: different thermal capacity

## Slide 27: What is the best possible effect?

## Slide 28: Minimal temperature estimation
Analogical phenomenon: Assman psychrometer
Wet and dry thermometer
Wet is cooler due to evaporation
Equilibrium state:
Solution:
Sufficient airflow

## Slide 29: Wet bulb vs. refrigerator
Chart: time [min]
wet bulb temperature | 17 | 17
We can get close to the theoretical minimum

## Slide 30: Minimal achievable temperature
Chart: 

## Slide 31: Best cooling effect
Sufficient air flow
  volatile liquid with low concentration in air (eg. Ethanol)
  Minimise thermal capacity of the fridge (eg. Low outer pot)
Maximize the area of evaporation
speed
Minimal temperature

## Slide 32: Thank you for your attention
Chart: 

## Slide 33: APPENDICES

## Slide 34: Assman psychrometer theory
Assumptions:
Air cools to Tfridge; vapor pressure saturates
(thanks to fast airflow)
Equilibrium of heat flow:
Numerically solve for
(complicated function )
Wet bulb

## Slide 35: Extra measurements

## Slide 36: Airflow importance
Chart: Time [min]
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135
enviroment | 20.7 | 20.6 | 20.5 | 20.4 | 20.3 | 20.3 | 20.2 | 20.2 | 20.2 | 20.2 | 20.3 | 20.2 | 20.2 | 20.2 | 20.1 | 20 | 19.9 | 19.8 | 19.7 | 19.7 | 19.7 | 19.6 | 19.4 | 19.6 | 19.6 | 19.6 | 19.6
no fan | 18.2 | 18 | 17.8 | 17.7 | 17.6 | 17.5 | 17.4 | 17.3 | 17.3 | 17.2 | 17.2 | 17.2 | 17.2 | 17.2 | 17.1 | 16.9 | 16.8 | 16.7 | 16.7 | 16.6 | 16.6 | 16.4 | 16.4 | 16.3 | 16.3 | 16.4 | 16.2 | 16.2
fan | 18.4 | 18.1 | 17.7 | 17.2 | 17 | 16.6 | 16.3 | 16.1 | 15.9 | 15.8 | 15.7 | 15.6 | 15.6 | 15.5 | 15.2 | 14.9 | 14.7 | 14.4 | 14.3 | 14.1 | 14.1 | 14 | 14.1 | 14 | 14 | 14.1 | 14.1 | 14.1

## Slide 37: Water vs. ethanol: Rate of evaporation
Chart: time [s]
| 0 | 100 | 120 | 140 | 170 | 190 | 220 | 250 | 270 | 290 | 310 | 340 | 360 | 380 | 400 | 430 | 450 | 480 | 510 | 530 | 550 | 580 | 630
ethanole | 38.6 | 37.4 | 36.85 | 36.4 | 35.7 | 35.35 | 34.9 | 34.3 | 34 | 33.6 | 33.2 | 32.7 | 32.4 | 32 | 31.65 | 31.1 | 30.8 | 30.2 | 29.75 | 29.4 | 29 | 28.4 | 27.7
water | 44 | 43.4 | 42.85 | 42.1 | 41.15 | 40.87 | 40.5 | 40.2
 Ethanol: more volatile

## Slide 38: Do we need cloth or not?
Chart: Cloth
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110
Cloth, Sand, Water | 19.7 | 19.4 | 18.9 | 18.3 | 17.9 | 17.7 | 17.6 | 17.2 | 16.9 | 16.8 | 16.7 | 16.5 | 16.4 | 16.4 | 16.3 | 16.3 | 16.2 | 16.2 | 16 | 16 | 15.9 | 15.9 | 15.9
Sand and a lot of water | 21.2 | 21.3 | 21.3 | 21.1 | 21.1 | 21.1 | 21.1 | 21.2 | 21.2 | 21.2 | 20.9 | 21.3 | 21.3 | 21.3 | 21.4 | 21.4 | 21.4 | 21.5 | 21.5 | 21.5 | 21.5 | 21.6 | 21.6
Sand and a little of water | 20.1 | 20.2 | 20.1 | 19.9 | 19.9 | 19.7 | 19.7 | 19.6 | 19.6 | 19.6 | 19.5 | 19.6 | 19.6 | 19.6 | 19.6 | 19.7 | 19.8 | 19.7 | 19.8 | 19.7 | 19.8 | 19.8 | 19.9
Environment | 22.7 | 20.2 | 20.3 | 20.6 | 20.7 | 20.7 | 20.8 | 20.8 | 20.9 | 20.9 | 21 | 21 | 21.1 | 21.2 | 21.3 | 21.2 | 21.2 | 21.1 | 21.2 | 21 | 20.7 | 20.6 | 20.6
Only water | 20.5 | 20.1 | 20.1 | 20.4 | 20.6 | 20.9 | 21 | 21.1 | 21.3 | 21.4 | 21.4 | 21.4 | 21.5 | 21.5

## Slide 39: What is the best material for cloth?
Chart: time [min]
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135
Fluffy cloth | 18.5 | 18.3 | 18 | 17.7 | 17.5 | 17.4 | 16.9 | 16.8 | 16.5 | 16.4 | 16.3 | 16.2 | 16.1 | 15.9 | 15.8 | 15.5 | 15.3 | 15.2 | 14.9 | 14.8 | 14.7 | 14.6 | 14.4 | 14.3 | 14.2 | 14.2 | 14.2
Normal cloth | 18.4 | 18.1 | 17.7 | 17.2 | 17 | 16.6 | 16.3 | 16.1 | 15.9 | 15.8 | 15.7 | 15.6 | 15.6 | 15.5 | 15.2 | 14.9 | 14.7 | 14.4 | 14.3 | 14.1 | 14.1 | 14 | 14.1 | 14 | 14 | 14.1 | 14.1 | 14.1
enviroment | 20.7 | 20.6 | 20.5 | 20.4 | 20.3 | 20.3 | 20.2 | 20.2 | 20.2 | 20.2 | 20.3 | 20.2 | 20.2 | 20.2 | 20.1 | 20 | 19.9 | 19.8 | 19.7 | 19.7 | 19.7 | 19.6 | 19.4 | 19.6 | 19.6 | 19.6 | 19.6

## Slide 40: Why the type of cloth does NOT matter?
1) Water fills gaps
Water fills gaps.
The surface of water = the area of evaporation
 The same as normal cloth
Area of evaporation
=
area through which heat gets in
Equilibrium temperature doesn’t change
2) Water soaks

## Slide 41: Effect of different sizes

## Slide 42: Effect of different shapes

## Slide 43: Our refrigerator

## Slide 44: Covered VS uncovered areas
Height of cloth
Uncovered areas  heat gets in
Covered areas
 Evaporation + heat gets in

## Slide 45: Does area of cloth matter?
Chart: The height of cloth
| 9 | 7 | 5 | 3 | 1 | 0
Temprature[C] | 16.41 | 16.845 | 17.5 | 18.53 | 19.74 | 20.1325
Whole fridge must be covered

## Slide 46: Why istn’s the second pot needed?
Area of evaporation
=
area through which heat expands
We do not need the second pot
only requirement for fridge’s surface
…ISOLATED AREAS MUST BE UNCOVERED WITH CLOTH
So that area of evaporation
=
area trough heat gets in

## Slide 47: Speed of cooling
k1= ability of liquid to evaporate [kg/m3]
k2= part of air which cools down [J/Km3]
Temperature difference
1/tau
Properties of liquid

## Slide 48: Assman psychrometer: theory
Equillibrium of heat flow:
Air cools to Tfridge; vapor pressure saturates:

## Slide 49: Assman psychrometer: theory
Surrounding air:
  Transfers heat to the cloth:
  Absorbs water vapor (heat used for evaporation)
Equilibrium (terminal temperature):

## Slide 50: Minimal T: theoretical estimation
Terminal temperature:
Numerically solved for
(complicated function )

## Slide 51: Conclusion – What should the most effective refrigerator look like?
Minimal temperature:
  sufficient air flow, maximize evaporation area
  volatile liquid with low concentration in air (eg. Ethanol)
Fastest cooling:
  Fast air flow
  Minimise thermal capacity of the fridge (eg. Low outer pot)
Prediction of minimal temperature